## Slide 1: The Step Command: A Closer Look
By: Kripa Varma

## Slide 2: Contents
Introduction
GDB Internals
pyOCD Internals
cmsis_DAP Interface Internals
Serial Wire Debug Protocol
Conclusion

## Slide 3: Introduction
(gdb) step
- tells a halted target to execute one instruction and then halt
gdb repeats this in a loop, if one line of code involves multiple instructions

## Slide 4: (gdb)step ---> DHCSR.C_STEP
gdb <-> pyOCD
RSP Packet
pyOCD <-> cmsis dap I/F firmware
DAP Command
cmsis dap i/f <->ARM Cortex M3
Serial Wire Debug Protocol

## Slide 5
inf
cli
target
remote
arm-none-eabi-gdb
pyOCD
gdb_server
Target cortex_m
Transport cmsis_dap
Interface pyUSB_backend
DAP
USBD
USBD_ HID
SW_DP
Dbg Port
Mem Acc Port
CMSIS DAP I/F firmware
serial
ser-tcp
gdb_socket
Beagle 5000 USB Protocol Analyzer
TCP
IP
USB HID
RSP
DAP Cmds
SW_DP
GDB
LPC11U24
LPC1768
Host PC
Mbed module
S/M bus
The System

## Slide 6: Contents
Introduction
GDB Internals
pyOCD Internals
cmsis_DAP Interface Internals
Serial Wire Debug Protocol
Conclusion

## Slide 7: GDB Internals
CLI : Command Line Interface
MI : Machine Interface
BFD : Binary File Descriptor
ELF DWARF : Debug format for ELF file
INF : Inferior execution control

## Slide 8: GDB- RSP Packet
gdb -> pyOCD
step command RSP packet :
$s#73

## Slide 9: GDB - Step Command backtrace

## Slide 10: pyOCD Internals
board (mbed_board)
flash (flash_lpc1768)
target (cortex_m)
transport (cmsis_dap)
interface (pyOCD_backend)
gdb_server

## Slide 11: Contents
Introduction
GDB Internals
pyOCD Internals
cmsis_DAP Interface Internals
Serial Wire Debug Protocol
Conclusion

## Slide 12: pyOCD - backtrace
gdbserver/gdbserver.py: run() handleMsg() step() target/cortex_m.py: step() writeMemory(DHCSR, value) transport/cmsis_dap.py: writeMem() // called twice , 1st TAR, 2nd DRW dapTransfer() // imported from cmsis_dap_core.py interface/pyUSB_backend.py: write() ep_out.write() // call pyUSB

## Slide 13: DAP Command Format
DAP Command Format:
CmdId(8), DAPIdx(8), count(8), { { req1 (8), data1 (32) }, { req2 (8), data2 (32) }, …. }
  Where Req = RegAddr[3:2], RnW(1), APnDP(1)
Reg Addr Values :
  b00 = CSW
  b01 = TAR // Target Address
  b11 = DRW // Data Read Write
{C_STEP, C_MASKINTS, C_DEBUGEN } -> DHCSR
0x5, 0x0, 0x2,{ 0x5,0xE000EDF0, 0xD, 0xA05F000B}
1st Req: Write 0xE000EDF0 to AccessPort Reg TAR
2nd Req: Write 0xA05F000B to AccessPort Reg DRW

## Slide 14: USB Analyzer Capture

## Slide 15: Contents
Introduction
GDB Internals
pyOCD Internals
cmsis_DAP Interface Internals
Serial Wire Debug Protocol
Conclusion

## Slide 16: Overview
3 Interfaces / Function
  Mass Storage Device ( for Drag n Drop F/W upgrade)
  * Bulk EP #2
  Human Interface Device (for CMSIS_DAP Debugging )
  *INT End points #1
  Communication Device Class ( for serial comm,
  USB-UART bridge)
  *Bulk EP #4
  *INT IN EP #3 for keep alive messages

## Slide 17: CMSIS_DAP I/F Firmware

## Slide 18: CMSIS_DAP Backtrace
USBD_LPC11Uxx.c : USB Driver Interrupt handler sets EP OUT Event USBD_HID.c : HID_EP_INT_Event () task wakes up Invokes USER_HID Callback.
USB_USER_HID.c : Sets DAP_PAQUET_RECEIVED event hid_process() task wakes up DAP.c : DAP_ProcessCommand(request, response) DAP_SWD_Transfer(request, response) SW_DP.C : SWD_Transfer(request, response) SW_WRITE_BIT()

## Slide 19: Contents
Introduction
GDB Internals
pyOCD Internals
cmsis_DAP Interface Internals
Serial Wire Debug Protocol
Conclusion

## Slide 20: Serial Wire Debug Protocol
The transactions over Serial Wire for writing DHCSR address (0xE000EDF0) to TAR register of Mem AP
1 | 1 | 0 | 1 | 0 | 0 | 0 | - |  | 1 | 0 | 0 |  | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1

## Slide 21: Debug Access Port
Data [32] | A[3:2] | RnW | APnDP
AHB AP
Bank1 |  |  | 
Bank0 |  |  | 
DRW |  | TAR | CSW
APB AP
Bank1 |  |  | 
Bank0 |  |  | 
DRW |  | TAR | CSW
Debug Port |  |  |  |  |  | 
 |  |  | SELECT | CSR | IDCODE | ABORT
System Memory Space
DBG Reg |  |  |  | 
DEMCR | DCRDR | DCRSR | DHCSR | DFSR
AHB BUS
4 Banks per AP
?
0
1
DAP Req
JTAG AP
Debug Port
Access Port
Select.APSEL(8): chooses AP.
Select.APBANKSEL(4): chooses bank.
A[3:2]: selects register

## Slide 22: Thank you